PSAS Autonomous Recovery System

Abstract:

The Portland State Aerospace Society, a group formed by the PSU AESS, plans to utilize an autonomous recovery system for its future launch vehicles.  It will consist of a parafoil (ram-air parachute) steered by a mechanical device controlled by a microcontroller.  The microcontroller will monitor various environmental and dynamic variables, as well as an electronic compass and a GPS module.  The recovery system will steer booster stages and payloads back to a pre-determined point for safety and easy recovery.

The PSU Capstone project has been broken down into phases which begin with research into parafoil theory and progress into designing and building the mechanical shroud line controller and associated electronics and firmware.  The firmware will implement a basic set of rudimentary shroud line control commands which will be communicated via an RF link.  This will provide a means to remotely steer the parafoil and 5-20 kg payload.  If time allows, the project can continue to develop fly-by-wire and then completely autonomous control using appropriate steering algorithms and information from the electronic compass and GPS module.

Team:

We're looking for a small team, between 1 and 3 people, to work closely with the PSAS.

Requirements:

·	Prior engineering experience in industry.

·	Interest in embedded control (microcontrollers) and aerospace.

·	Ability to design and build electronic and mechanical components, as well as write the firmware (i.e., some experience with C or assembly language).

For more information:

Primary contact:	Paul Glasser  (paul@glasser.com)

Other contacts:	Andrew Greenberg (drew@uad.com)

Brian O'Neel(oneelb@europa.com)

Web page:		http://www.ee.pdx.edu/~aess

How we envision doing this:

The parafoil will be steered by adjusting control lines to deflect a portion of the trailing edge.  This deflection creates a yaw moment which results in a sidded turn in the direction of the deflected side.

One method for control line adjustment might be to connect opposite control lines end-to-end and vary the location on the connected lines from which the controller and load is suspended.  For example, the left control line would come down from the left shroud collection point, run through the actuator across a pinch roller, and then back up to the right shroud collection point.  A similar arrangement would be used for front to back control for flaring and collapsing. The actuator would rapidly “crawl” along the control lines, thus changing the ratio of the lengths of opposite control lines to effect a change in the parafoil’s attitude.  A scheme to power down and lock control line ratios would need to be employed so that battery energy can be conserved in between maneuvers.

One method for doing this might employ a system of ratchets with the ratchet controls energized by solenoids.  Another might use a lightweight gearset to multiply the torque required to turn over the motor’s rotor when no current is applied.

The motor will be controlled by a PIC microcontroller residing on a CANbus, which is monitoring whatever system dynamics will be required to keep the parafoil stable and steerable.  We would also like to monitor ambient pressure, as well as airspeed.  A CANbus module containing a 2-way digital RF link will be provided for communications with the ground.

We’ve broken the task into sequential phases:

Phase 1 – research

We need the following questions researched and a short paper presented summarizing the answers:

General parafoil theory and designs:

·	Are there different varieties of parafoils?

·	What kinds of basic shapes of parafoils are utilized?

·	What are different parts of the parafoil called?  What is the terminology used?

·	How are the designs modified, and for what purpose? (i.e. flaps to spill air?)

·	What are the design tradeoffs? (i.e. maneuverability vs. stability)

·	Are some designs less sensitive to load variations?

·	What are typical useful/requisite maneuvers? (i.e. turn, glide, reduce/increase speed, flare, collapse)

·	How is each maneuver done?

General parafoil design for the PSAS:

·	What parafoil design (shape, aspect ratio, wing loading) is best for us?

·	What are the number and location of shroud lines?

·	What kind of shroud line maneuvering is required to steer and flare?

·	What sensors will be required to assist in various maneuvers?

Specific information needed to design a parafoil and controller:

The following information needs to be defined in a manner so that we can see the relationship between different variables as parameters vary and use the resulting information to simulate various designs and conditions.  Specific mathematical functions should be supplied whenever possible.

·	How much tension will the shroud lines have under expected loading conditions?

·	How much force will be required on the control lines to perform the required maneuvers?  This force depends on the mass of the load under the control line and how fast the mass is accelerated, or how fast the control line must be shortened.

·	What are the dynamic characteristics of the control forces required on individual control lines to achieve each maneuver under different environmental conditions?

This question must be answered with enough specificity to choose an actuator (motor and gearing components) for any set of parafoil size and load conditions.  Later, this question will need to be answered more specifically in order to design autonomous steering algorithms.

·	How do we determine how to scale the parafoil design to achieve desired glide angle, lift capacity, etc. for a given air density?

·	For a given design, how do we determine upper and lower bounds for load?

·	What are limits for magnitude and frequency of load/shock cord vertical oscillation?

·	How do we determine the appropriate shock cord length and spring constant? (This is of course load-dependent.  We need a graph here to make this easy for someone to calculate.)

Phase 2 – selection of a parafoil

We will use the information from Phase 1 to obtain a small parafoil to use to verify the design concept.  It would be preferable to utilize an off-the-shelf parafoil kite if a suitable model is available.  Control lines may need to be modified or added.

Document above.

Phase 3 – design of the mechanical controller and electronics

Selection of mechanical components (motors, solenoids, gear, ratchets, pinch rollers, etc.).

Selection of power source.

Design of electronics to control above.

PSAS will provide a GPS CANbus module and a 2-way rf 50kB modem CANbus module.

Selection of electronic components (determine size and location of circuit board and antenna).

Mechanical design and location of all components in a cylindrical housing suitable for deployment.

CAD drawings (2D or 3D, must be saved in AutoCAD dwg format).

Schematics (use Eagle freeware).

Phase 4 – construction and verification of controller hardware

All mechanical components assembled and tested in housing.

A simple jig to test actuators should be built so that operation and torque levels can be verified.

Document operation of test jigs.

Assembly of all electronics on a breadboard.

Write enough firmware to verify rf link and interface to GPS, sensors, and actuators.

Document firmware.

Phase 5 – write firmware commands to enable remote fly-by-wire

Implement rudimentary low-level commands for rf link and actuator control.

Document firmware.

Phase 6 – write firmware commands for autonomous control

Implement rudimentary low-level commands for GPS and sensor input.

Implement autonomous control using the low-level commands and appropriate algorithms.

Document firmware.

Phase 7 – summarize the project and write a paper

Design criteria:

Atmospheric Modeling: Use 1976 Standard Atmosphere Definitions.

Units: Except for mechanical hardware (fasteners, machining, etc.), all units are

to be metric.

Minimize Weight: Obviously, since this will be a system used in a rocket, we must minimize the weight of the system as much as possible. While for the prototype device this is not so much of an issue, the future design goals require an extremely light weight system (ounces matter!) so the initial prototype must be created with this future limitation in mind.

Minimize power: The motors (one for left/right, another for flair/collapse) will need to run off a battery, possibly a high-current NiCd or Ni metal hydride.  It could be a DC servo motor or a permanent magnet stepper motor, but keep in mind that if a stepper is used we do not want to have to maintain current (draws too much power) between maneuvers, and thus we cannot rely upon the stepper current to hold tension on a control line. We should be able to remove power from the actuator once the attitude has been adjusted, and then rely upon a lightweight plastic gearset or some other means to maintain attitude.  This will be required during periods of unbalanced control line tension, which will occur during maneuvers and steady state flight due to wind gusts and a swinging and/or bouncing load.

Size: The controller and actuator will need to fit inside a cylinder of diameter 15 cm (9 cm would be preferable) and be as short as possible.

Shape and orientation: The control line connection should be designed to ensure that the controller and parafoil can be deployed properly.  PSAS will design and construct method of deployment, but the parafoil and airframe teams will need to work closely here.