## Portland State AESS / PSAS  			 Launch Vehicle No.2

Airframe General Design Principals:

# Principal				Reason

Simple as Possible: 			- Easier to fabricate.

- Easier to assemble.

- Lower construction time.

- Higher operational reliability.

- Easier to set up and operate.

- Easier for other teams to understand operationability.

- Easier to model.

Modular:				- Allows for future changes / upgrades.

- Allows flexibility to achieve a wide variety of goals.

- Damaged parts can easily be changed without having to

replace entire airframe.

- Allows other teams to keep their entire system up until

integration time.

Use Prior Experience:		- Use what we have learned already.

(we know what works, and what doesn’t)

Light Weight:			- Higher altitude for given Impulse.

- Challenge teams to be innovative.

Rugged:				- Able to stand up to repeated tests.

- Able to stand up to flight stresses.

- Will be handled back and forth between teams.

Cost Effective:			- Increase chance of completion within limited budget

- Low cost will be more attractive to sponsors.

Safety:					- Insure that no one gets hurt.

- Insure that no property gets damaged.

- Insure that no equipment is damaged.

Airframe (General) Design Goals:

Mission Statement: Efficiently, reliably, and repetitively deliver a payload to a

given altitude, in a controlled manner then safely return to earth.

Consideration				Goal

# Altitude				- 50,000 – 60,000 feet maximum altitude with empty vehicle.

# Payload				- Significant size ride-a-long payload module.

# - 6 inch dia. x 36 inch length. (cylinder)

# - 20 LB capacity.

# Efficiency				- 50% mass ratio, fuel to total weight, (minus payload).

# Control				(Passive guidance for maiden flight)

# - 3:1 Stability margin.

# - 5:1 Thrust to weight ratio.

# - Anti-roll flight.

Return				- Recoverable over a wide variety of circumstances.

Reliability				- 95% success in ground testing systems.

Repeatability				- Minimum life span of components should be 10 flights.

Airframe (Specific) Design Goals:

Goal 						Reason

# “P” Motor (60lbs fuel)				- In the realm of the possible without too much of an

investment of time or money.

# Total airframe weight 40lbs			- Will keep mass ratio near 50% for given fuel and

payload weight.

Break-away launch lugs			- Build upon previous knowledge.

- Removes perturbance from air stream.

Modular fin canister				- Lightweight, minimizes required airframe.

- Fins can be reduced as active guidance increases

- Fins easily replaced if damaged.

Rollerons 					- Simple method of roll stabilization.

- Inexpensive.

3-stage recovery system			- Ballistic recovery system for terminal velocity save

- Will be able to manually deploy at anytime after

apogee and still recover vehicle.

Single charge push recovery 			- Reduces complexity, no complicated mechanics.

- Minimal obstructions inside airframe.

Single seam nose separation			- Minimal separation force needed.

- Vehicle recovers as one piece.

- Easier to switch over to ballistic dart option.

Adjustable nose ballast			- Allows for adjustable CG for specific mission /

vehicle configuration.

Payload canister (extractable at apogee)		- Makes extraction predictable and reliable.

- Fixes geometry for independently developed ride-

a-longs.

- Fixes  avionics data -> payload  connections.

# Wire conduit from avionics to payload	- Fixes wire placement to keep it from interfering

with modules.

- Acts as index / guide for payload module.

- Acts as “push-off” for nose separator.

Strong load bearing z-axis structure		- To support Avionics and ATV modules.

- To support heavy payload modules.

- To support stress of recovery system.

All modules indexed / keyed			- Aid in alignment of components during integration.

- Aids in holding modules in position.

Minimal air stream perturbations		- Lower drag = higher altitude.

Sleeve coupling between sections		- Maximizes area inside airframe.

- Acts to align airframe.

- Minimizes obstruction inside airframe. Which

aids in extraction of modules.

Cartridge type pyrotechnics			- Rugged, modular, waterproof.

- Can be standardized.

- Can be pre-made.

Modular autonomy				- Each airframe module, once completed, can

be removed and worked on by specific team.

Up to time of integration w/o inhibiting another

team due to the need for that module.